## Slide 1: Disinfection and sterilization
Assist. Prof. Vojislav Ćupurdija
Faculty of Medical Sciences
University of Kragujevac
IASM - Introduction to clinical practice

## Slide 2: Technique and methods of disinfection
Disinfection represents the destruction of those microorganisms to which a disinfectant has been applied in a certain concentration, exposure time and environmental conditions
The purpose of disinfection is the targeted reduction of the number of unwanted microorganisms by chemical or physical procedures so that they are not able to cause an infection under the given circumstances.

## Slide 3: Technique and methods of disinfection
The main routes of infection are:
  Aerogenic
  Alimentary
  Contact
  Transmissive
Pathogenic germs most often enter the body through:
  Respiratory organs
  Digestive organs
  Mucous membranes and damaged skin

## Slide 4: Physical disinfection procedures
Effect of heat
Effect of hot water - washing dishes and laundry at 100°C
Cooking
Pasteurization – inactivation of vegetative forms of bacteria and fungi
Steam disinfection
Incineration – in special furnaces
Annealing – for simple metal instruments
Crossing with flames
Ultraviolet radiation

## Slide 5: Chemical disinfection
Agents for chemical disinfection work by removing water (dehydration), absorption, precipitation of proteins, changing the acidity of the environment and chemical reactions.
  1. alcohols - ethyl alcohol 70-80% and isopropyl alcohol 50-60%, for hand skin disinfection
  2. iodine - elemental iodine in an alcoholic solution (iodine tincture), for disinfecting dirty wounds and elemental iodine bound to an organic polymer - a disinfectant for mucous membranes and rinsing body cavities
  3. potassium permanganate – oxidizing agent for rinsing
  4. halogen elements - hypochlorites, chlorinated lime, milk of lime, organic chloramines
  5. organic compounds of mercury - phenyl mercury perborate, bacteriostatic for disinfecting wounds and mucous membranes, as well as for rinsing cavities

## Slide 6: Personal protection of medical workers
Work clothes and shoes
Protective masks
In the operating room and protective caps
Protective gloves
Regular hand washing with warm water and soap

## Slide 7: Disinfection of hospital premises
Regular washing and cleaning
Ventilation of rooms
Wiping surfaces with disinfectants
Application of UV lamps for 12 to 18 hours for full disinfection of the premises
Restriction of entry to unauthorized persons in rooms reserved for medical and support staff
Regular health checks of medical and support staff

## Slide 8: Disinfection of patient excreta
Sputum
Feces
Vomited content
Urinals
Stool collection pans
Glassware and other dishes

## Slide 9: Disinfection of instruments
In medical practice, the rule applies - first disinfect, and then wash the instruments that are in repeated use

## Slide 10: Sterilization
A procedure that completely destroys all organisms and their spores from objects, materials and instruments
methods :
  1. moist heat sterilization
  2. sterilization by dry heat
  3. sterilization by chemical means and the action of ultraviolet rays
  4. modern sterilization methods

## Slide 11: Moist heat sterilization
Sterilization by cooking
  The material to be sterilized is placed in a metal box, poured with distilled water that boils for 30 minutes
  Today, this method of sterilization is used only in extraordinary circumstances (war, natural disasters, earthquakes).
Sterilization in an autoclave
  Using superheated, saturated steam under pressure
  The autoclave has double boilers, the material for sterilization is placed in the inner one, and distilled water to a certain level is placed in the outer one

## Slide 12: Dry heat sterilization
It is performed in a sterilizer in which the instruments are exposed to the action of hot air at a certain temperature (180°C) and for a certain time (80 min).
The sterilizer box has two shells, an outer one made of sheet metal and an inner one made of aluminum, on which there are partitions for placing instruments and other items for sterilization.
It is used for metal instruments, glass syringes and porcelain objects

## Slide 13: Modern methods of sterilization
Sterilization by chemical means
Sterilization by ultraviolet rays - air in operating rooms
Express autoclave - for rapid sterilization of medical instruments, textile materials and rubber objects with dry saturated steam
Automatic steam sterilizer - performs sterilization with dry saturated steam under pressure

## Slide 14: Modern methods of sterilization
Dry sterilizer with accelerated cooling - hot air sterilization
Sterilization using ultrasound - in the food and pharmaceutical industry, less often for medical purposes
Sterilization using ionizing radiation
Sterilization with ethylene oxide - cold sterilization for items made of plastic, rubber, leather, devices, tubes and parts of devices for endotracheal intubation

## Slide 15: Types and application of antiseptics
Antiseptics and disinfectants represent the same compounds, which are called differently depending on the concentration
They represent substances that remove bacteria from the skin or objects - if they are in lower concentrations, then they are antiseptics (bacteriostatics), if they are in higher concentrations, then they are disinfectants (bactericides).
  Hydrogen peroxide - in the form of a 3% solution for skin disinfection and wound cleaning
  Boric acid - in the form of a 2% or 3% solution, for poultices in case of ulcers, erysipelas, burns
  Potassium permanganate - in the form of a 1% solution, for surface disinfection of the skin
  Alcohol - 70% ethanol alcohol, as an antiseptic
  Iodine - aqueous or alcoholic solution of iodine, as antiseptics for skin, mucous membranes or wounds
  Chlorhexidine - non-toxic antiseptic, for cleaning the skin and mucous membranes, hygiene of the oral cavity, cleaning surgical equipment, hands before operations, skin wounds...
  Resorcinol - phenolic antiseptic, used in dermatovenerology