## Slide 1
University of Kragujevac The Medical Faculty Integrated academic studies of medicine Physical medicine and rehabilitation
The first module
The third unit
ELECTROTHERAPY -Direct current-
Docent Dr. Igor Simanic

## Slide 2
Electrotherapy
A type of physical therapy which uses electrical energy
Electrochemical stimulus
Has an effect on
    Nerve receptors and nerves
    Cells and tissues it passes through.

## Slide 3
History of electrotherapy
Roman physician Scribonius Largus,
  A type of frog (Pedanios dioscorides).
  Touch of fish Torpedo marmorata,

## Slide 4
History of electrotherapy
Gilbert discovered electricity in 1600.
Galvani discovered the constant direct current in 1789, thorough experiments(Galvanic current).
Volta constructed the first artificial source of Galvanic current in 1789.
English physicist Faraday discovered alternating current of low frequency in 1831 (faradization)
D’Arsonval, a French biologist, introduced alternating current of high frequency into therapy in 1892.

## Slide 5
Classification of electrotherapy
Direct currents
Constant direct currents
Impulse direct currents
Alternating currents
Low-frequency
Medium-frequency
High-frequency

## Slide 6
Direct currents
Direct currents (frequency 0)
1. Galvanic direct currents are used as:
а) stable galvanization
2. Special forms of the use of Galvanic current:
    а) negative electrolysis
    б) ionophoresis
    ц) hydrogalvanic (hydroelectric) baths
    д) drug electrophoresis
Impulse direct currents ( to 1000 Hz)
    а) Leduc’s current
    б) Bernard’s currents (DDC)
    ц) exponential currents (Kovarscik)
    д) modulated currents

## Slide 7
Alternating currents
III Static electricity (franclinization)
IV Alternating currents
1. Low-frequency currents (frequency up to 1000 Hz)
    а) Farad current
    б) transcutaneous electrical neural stimulation (TENS)
2. Medium-frequency currents (frequency over 1000 Hz)
    а) medium-frequency currents- interferential Nemec currents
    б) sinusoid-modulated currents (Russian stimulation)
3. High-frequency currents (frequency over 100.000 Hz)
    а) D’Arsonvalization (frequency 100.000 Hz)
    б) Long-wave diathermia (frequency 500.000- 1.000.000 Hz)
    ц) short-wave diathermia (SWD) frequency 10-100 МHz
    д) ultra-short diathermia (frequency 434,78 МHz)
    е) microwave diathermia (frequency 2.450 МHz)

## Slide 8
Galvanic current
    Does not change its course.
    Does not change its intensity or voltage,
based on the feature of polarity

## Slide 9
PRIMARY (PHYSICAL) EFFECT
Chemical changes (ionic effect)
Electrokinetic changes (related to electro-osmosis and diffusion)
      Anaphoresis and
      Kataphoresis

## Slide 10
Chemical changes (ionic effect) on electrodes
+
NaOH
NaOH
HCL
HCL
+
+
+
+
+
+
Cl
H
OH
Na
+
H
Na
+
OH
NaCl
H2O
H2O
ANODE
CATHODE
Colliquative necrosis
Coagulation necrosis
2Na + 2HOH = 2NaOH + H2
      4Cl + 2HOH = 4HCl + 02

## Slide 11
Primary effect of poles
Anode
Acid medium
Analgesia
Anti-edematous effect
Calming effect
Cathode
Basic medium
Increase of sensitivity to pain
Accumulation of water
Irritating effect

## Slide 12
SECONDARY (PHYSIOLOGICAL) EFFECT
Conditioned by having an effect on:
Nerve endings and receptors
    Vasomotor – vasodilation(in the skin and muscles)
    Motor nerves – muscle tone (anelectrotonus and cathelectrotonus
    Sensory nerves – improves afferentation of the external and proprioceptive sensibility
    Pain receptors – pain modulation(analgesia below an anode).
On cells and tissues
    Increases permeability of cellular membranes
    Activity of cellular enzymes
    metabolism
    Positive TROPHIC effect
    Affects REGENERATION PROCESS

## Slide 13
THERAPEUTIC USE
  Improvement of arterial and venous circulation with an increase of the blood flow of the skin muscles and other tissues through which Galvanic current passes,
  Absorption of extravasates and elimination of metabolites,
  Reduction of pain and reduction of irritability of the sensory nerves,
  Increase of the motor nerve irritability,
  Improvement of the biological cell activity,
  Improvement of the tissue mass,
  Improvement of the reparation and regeneration process

## Slide 14
Use of Galvanic current
Longitudinal galvanization, when the electrodes are set on the endings of the treated segment, or down the extremity;

## Slide 15
Application of Galvanic current
Transversal galvanization, when a treated segment is between the electrodes.

## Slide 16
Dosing of Galvanic current
  Amperage (мА),
  Surface area of electrodes (cm2)
  Current density (мА/cm2)
  Duration of procedure(10 to 20 min)
  Number of procedures in one series
  Series= 10 procedures

## Slide 17
Indications for application of Galvanic current
    In neurology:
    -diseases and injuries of the peripheral nerves, neuralgia, neuropathy, radiculopathy
    -myalgia, atrophy and paralysis of muscles
    In orthopedics:
    -post-traumatic conditions in which the skin is intact
    Rheumatic diseases in chronic phase
    Vascular diseases in phases I-II according to Fonten (endartetitis obliterans, atherosclerosis, diabetic vasculopathy, Rein diseases)
    Frostbites
    In trophic changes and edemas
    In electrodiagnostics

## Slide 18
Contraindications for the use of Galvanic current
    Bleeding and bleeding tendency;
    Febrile conditions and infective conditions
    cachexia;
    In the domain of local acute inflammation (joints, lungs etc.);
    Cardiac and vital organ decompensation;
    Tuberculosis
    malignant tumors
    thrombophlebitis
    Presence of metal on the site of application
    Skin defects on the site of electrode application

## Slide 19
Special forms of application
    Negative electrolysis (dermatology)
    Ionophoresis (dental medicine)
    Hydrogalvanic baths
    Drug electrophoresis

## Slide 20
Hydrogalvanic (hydroelectric) baths
Tissue galvanization is performed in special baths made of plastic mass filled with water and with the graphite electrodes set on its walls.
The tubs are intended for local and general hydroelectric bath.

## Slide 21
Local hydroelectric bath
Is applied in one or several tubs (cells), into which an extremity segment is immersed, most often a hand or foot. There are one-cell, two-cell, and four-cell baths (for all four extremities).
Tap water is poured into the tabs, Т=36-37ºC, into which a patient puts his arms, bent at the elbows, up to the lower third of the upper arm, and legs, up to the middle of the lower leg, then electricity is turned on and the polarity of electrodes is chosen.

## Slide 22
General hydroelectric bath (hydrogalvanic tub)
Is performed in a big tub (Galvanic tub), equipped with several big electrodes and is used for galvanization of the whole body, except the head.
A patient assumes a semi-sitting position in a tub.
Depending on the polarity of electrodes, there is a possibility of multiple combinations.
The current strength is 300 to 500 mА and the procedure lasts for 15 to 20 minutes.
If a patient has skin defects, they should be rubbed with vaseline.

## Slide 23
4. Medicinal electrophoresis
Тranscutaneous drug administration throgh the intact skin via galvanic current.
      If a medicine is soluble in water and
      If it is dissociated in a water solution.

## Slide 24
The most common used medicines for electrophoresis
The anode electrophoresis includes:
  Novocain
  Histamin
  Redergin
  Corticosteroids

## Slide 25
The most common used medicines for electrophoresis
The cathode electrophoresis:
  Potassium-iodid
  Crystal penicillin
  Thiomucase.

## Slide 26
Benefits of medicinal electrophoresis:
Long duration of procedure action-drug depot
Local action in a superficial pathological process,
Prevention of gastric intolerance and avoidance of hepatic blood flow,
Pain-free procedure

## Slide 27
Shortcomings of electrophoresis:
Difficult dosing decisions
A relatively long procedure(10 to 30 minutes),
Requires an apparatus for application of Galvanic current,
A medicine can be administered only through the intact skin.

## Slide 28
Direct impulse currents
IMPULSE – a single flow of low-intensity current in one direction, during a short, given time interval, with the pause.

## Slide 29
Direct impulse currents (frequency up to 1000 Hz)
а) Leduc's current
b) Bernard's (DDC) currents
c) exponential currents (Kovarscik)
d) modulated currents

## Slide 30
LEDUC'S CURRENT (Ultra-Reiz or ultrastimulating currents)
IMPULSE CHARACTERISTICS
Rectangle impulse
Impulse 2ms,
Pause 5ms,
frequency =140 Hz.

## Slide 31
LEDUC'S CURRENT
Physiological effect: these currents show local,vasodilatory, spasmolytic effect (decrease the tone of spastic and rigid muscles), as well as analgesic effect, whereby pain reduction is greater underneath a cathode, unlike Galvanic current, where an analgesic effect is greater underneath an anode. Indications: all painful conditions of the locomotive apparatus, muscle spasm and peripheral blood flow defects

## Slide 32
BERNARD'S (DDC) CURRENTS
Impulses with a semi-sinusoid shape,
Modulations: MF, DF, CP, LP, RS
Base and dose
Lasting for 10 ms, with a 10ms pause or without a pause, with a frequency of 50Hz or 100Hz.
Impulses of a relatively small amplitude, below the treshold of motor neuron activation.

## Slide 33
Indications for the use of DDC:
In acute ad chronic pain syndromes,
In soft-tissue injuries,
Rheuamtic diseases
Compressive radiculopathy
In initial stages of peripheral arterial diseases.

## Slide 34
EXPONENTIAL CURRENTS (Kovarscik)
Characteristics of an impulse
Triangular impulses or in a shape of an exponential curve
Exponential curve is characterized by mild increase and decrease of intensity.
Impulse lasts from 125ms to 2000ms,
A pause is twice as long.

## Slide 35
Parameters of exponential currents depending on the degree of the peripheral nerve lesion, or severity of paralysis of muscles.
Severity of paralysis
EXPONENTIAL CURRENT
Type
Duration of an impulse in ms
Duration of a pause in ms
Rest time between the series in minutes
Most severe degree of paralysis (grade "0", "1" by MMT)
E 2
500 – 1000
2000
2 - 2,5
Moderate degree of paralysis (grade "2", "3" by MMT) and all mimic musculature paralyses
E 1
250
500
1,5
Mild impairments (grade "3+", "4-" by MMT)
50 – 125
250 - 500
1

## Slide 36
Е1 type of exponential currents (used for eliciting muscle contractions in severe peripheral paralysis) Е2 type of exponential currents (used for eliciting muscle contractions in moderate peripheral paralysis)

## Slide 37
Indications for electrostimulation:
PPM:peripheral paralysis and central paralysis of muscles, atrophy due to inactivity
GM: of the urinary bladder and colon, incontinence, night urination
Prevention of thrombophlebitis in bed-ridden patients
Stimulation of osteogenesis

## Slide 38
Technique of electrostimulation
Bipolar technique
Monopolar technique
Number of contractions:
5-10x10
Duration of treatment:
grade3 by ММТ
Number of days: Unlimited

## Slide 39
MODULATED CURRENTS (Swelstrom)
Exponential impulses, lasting 10ms with a pause of 20 ms, whose frequency is 33Hz -basic frequency, and which lead to tetanic muscle contraction (muscle twitch), are modulated by intensity to obtain series of gradually increasing impulses (packs) with a pause in-between.
Lead to muscle contraction which is similar to the contraction of a valid muscle, and is more often used for lesions of the central motor neuron
Frequency of the modulated currents is measured in contractions per one minute (unlike the single impulse currents, where it is measured per 1 second), and usually amounts to 10-15-20 contractions per minute – frequency or rhythm of modulation.

## Slide 40
Electrostimulation of the deltoideus muscle and the extensors of the hand and fingers

## Slide 41
Indications for modulated currents
Therapeutic effect
Tetanic muscle contractions
Indications
Post-inactivity and post-immobilization hypotrophy of the musculature with the decrease of msucle power.
Paralytic musculature after a lesion of the central nervous system
Prevention of thrombophlebitis in bed-ridden patients
Stimulation of hypoplastic paravertebral musculature in scoliosis of the spine.
Stimulation of osteogenesis.

## Slide 42
Electrodiagnostics
Classic electrodiagnostics
  By neofarad and
  impulse galvanic current
Chronaximetry
Electromyography
  Detection electromyography
  Stimulation electromyography